## Slide 1
Mooring operation at Strömmen
For ships shorter than 230m
anchoring and mooring is still possible
Anchor
Mooring
For mooring click on the blue mooring path for anchoring green anchor path

## Slide 2: Mooring operation at Stockholm Ström

## Slide 3: The anchor system is similar, as the offshore industry use for mooring in open waters
2 x ”MK5”-anchor, weight of 15 tons each

## Slide 4
The blue and violett figurs show all of the anchors at Stockholms Ström

## Slide 5
There is ~ 10 m slack in the chain for each buoy which means that the distance between buoys will be ~380m after the lines has been tightened

## Slide 6
The system is designed for mean winds up to 14 m/s in all directions for a ship with a wind area of 10 000 sqm

## Slide 7
Maximum 6 lines can be used for mooring at the western buoy and 8 lines at the eastern buoy
The buoys are equipped with AIS and quick release hooks (SWL 125 ton) The anchor chain is the limitation for the buoy maximum work load for the buoy is 269 tons, break load 383 ton

## Slide 8
Stockholm Port do not have any restrictions for bow out or in. Its up to the ship to determine, but its appreciates if the ship will moor with the bow in
Its possible to approach north or south of the eastern mooring buoy

## Slide 9
If, mooring with the bow out, the yellowed marked area have an diameter of 340 m

## Slide 10
There is one mooring boat It is recommended to start with the moorings to the forward buoy
Before passing the eastern mooring buoy make fast the tug boat, tug line

## Slide 11
-just drop the lines, no heaving line required
The mooring boat will avoid working under tight lines and can handle two lines

## Slide 12
Before all lines are tight and fast the ship will swing for a while. It is important to give this operation some time and adjust the lines so bow and stern lines will be tightened

## Slide 13
On departure, slack lines so that the linesmen safely can embark the bouy
Dont let go more lines than the crew can bring in, to aviod any problems with lines in the propellers etc

## Slide 14
Anchor and buoy mooring at Stockholm ström

## Slide 15
Wind restrictions anchoring at Strömmen

## Slide 16
and can be presented in the chart and/or given to the mooring boat for an optical heading
The positions for the anchors are calculated from the mooring buoys position in the chart

## Slide 17
It´s possible to use western or

## Slide 18
- estern mooring buoys, but only between the two buoys

## Slide 19
At certain wind and current conditions, the ship drift southward during the approach
Connect the tugboat aft with tugs line

## Slide 20
Use the mooringboat for an optical heading to the dropping position.

## Slide 21
Manoeuver towards the mooringboat
Before the anchor drops, the mooringboat will move towards the other anchor position

## Slide 22
After the first anchor has been dropped, move the ship to the other anchor position. 7.5 shackles will be used to reach second anchor position.

## Slide 23
Max two lines at the same time for the mooringboat
Before the second anchor drops, the mooring boat will move to the mooring buoy.
When the other anchor has been dropped, the tugboat will assist/tow the ship towards the mooring buoy

## Slide 24
Maximum 6 lines can be used for mooring on the western buoy and 8 lines at the eastern buoy
The buoy is equipped with AIS and quick release hooks The anchor chain is the limitation for the buoy maximum work load for the buoy is 269 tons, break load 383 ton

## Slide 25
Well moored at Strömmen
Distance buoy – Ship 30-40m
Drift of buoy ~10 m
The bouy will pitch when the lines are tighted
5 Schackels
5 Schackels